# Wilson II X-axis assembly notes
Step by step notes / 1. insert the linear bearings into the X ends and X carriage / 2. Attach the lead screw nuts to each x end using two M3 x 14mm screws and nuts on each. / 3. Assemble the 624 bearing with the printed belt guides and the X tensioner (or use a preassembled idler pulley with the alternate x tensioner) using a M4x20mm screw and hex nut. Insert a M3 nut into the X tensioner and thread M3x30mm screw in just until through nut. Install the X tensioner in the X idler end, using a M4 x 20mm screw to secure the tensioner. / 4. Wire each endstop (if not prewired). Z endstop will need about 70cm of wire, the X axis only needs about half that. / 5. attach one endstop switch to the X motor end using a miniature zip tie (or two M2 screws and nuts). Secure with a zip tie through the slot provided on the X motor end. / 6. Attach one endstop to the Z pinion using a miniaturej zip tie. Secure wires using another zip tie through the small loop provided on the Z pinion to prevent strain on the wire. / 7. Slide the Z rack through the slot on the bottom of the X carriage, align the Z pinion, and secure pinion using a M3x20mm screw and hex nut. / 8. Attach the extension springs to the Z pinion. On each side of the X carriage, attach an extension spring with a M3x10mm screw into the holes provided. Tighten M3x10mm screws just until bottomed out. Thread a M3x40mm screw through one extension spring, then through the Z pinion, and attach the other extension spring to the other side of the M3x40mm screw. Attach a M3 locknut and tighten just until the screw is through the locknut. / 9. Install GT2 pulley onto the stepper motor and attach the stepper motor to the X motor end using three M3x14mm screws. / 10. Slide each 10mm smooth rod into one of the X ends, then slide X carriage onto rods, followed by the other X end. / Do not attach the timing belt yet (wait until you've mounted the X axis to the frame).	Parts needed: / Description Quantity / X Idler end 1 / X Motor end 1 / X tensioner 1 / X Carriage 1 / Z Rack 1 / Z Pinion 1 / 624 bearing belt guide (2 pieces) 1 / NEMA17 stepper motor 1 / GT2 timing pulley 1 / 624 bearing 1 / Lead screw nut 2 / Endstop switch 2 / LM10UU linear bearing 8 / 370mm 10mm smooth rod 2 / Miniature nylon zip ties (2mm width) 6 / M3 x 14mm screw 7 / M3 x 40mm screw 1 / M3 x 30mm screw 1 / M3 x 20mm screw 1 / M3 x 10mm screw 2 / M4 x 20mm screw 2 / M3 nex nut 5 / M3 locknut 1 / M4 locknut 1 / M4 hex nut 1 / 0.625” extension spring 2 / Tools needed / Phillips screwdriver / Allen keys / Plier